## Slide 1: EE577b Synthesis
Spring 2020
TA/Mentor: Soorya Ramesh
Professor: Dr. Moe Tabar

## Slide 2: Unzip Pre-Synthesis.zip
Paste in ee577b folder.
Run usual commands. (dff.v module name dff)
  make clean
  make sim (or) make simg

## Slide 3: Synthesis
Paste design file (dff.v) in src folder as well.
make syn
  In netlist folder, you will find
    dff.sdc
    dff.sdf
    dff.syn.v
  In report(s) folder, you will find
    dff.area
    dff.check_design
    dff.timing

## Slide 4: Synthesis
Command
  sim_syn
  Simulate the synthesized .v file without GUI.
  simg_syn
  Simulate the synthesized .v file with GUI.

## Slide 5: Make File
TOP = tb (tb file)
TOP_SYN = tb_syn (tb file for synthesis)
DESIGN_NAME = dff (design file)
Modify for your code as required.
All commands that can be used in NCsim can also be found here.

## Slide 6: Scripts
If you want to change period of clock for the synthesized file, you can modify it in syn.tcl

## Slide 7
Copy the normal tb file
Paste this line in your module where d1 is the name of your instantialtion (can be modified).
Include this line in your tb.

## Slide 8: Reports
Area Report
  Total cell area gives the are of the cell
Timing Report
  Slack has to be positive.
Check Design Report
  If there are no errors, it will show 1.